## Slide 1: unit 3.0
Wood

## Slide 2: Objectives
Correctly identify the differences between hardwood and softwood trees
Discuss the processing of the wood from tree to board in sequential order
Recognize standard molding patterns
Name and describe common lumber defects
Describe how the production, grading, and sale of hardwood and softwood lumber differ

## Slide 3: Objectives (continued)
Calculate board feet
Identify different types of grain and explain how they affect the appearance of wood
Describe wood movement and how it affects woodworking practices
Identify various woods and their individual characteristics
Identify sources for acquiring wood

## Slide 4: Introduction
Trees are a source of abundant materials
Virtually every part of the tree can be turned to our use
Trees provide the materials used to build and furnish our homes

## Slide 5: Hardwoods and Softwoods
Trees can be divided into two main categories:
  Hardwoods (deciduous)
  Softwoods (coniferous)
Parts of a tree
  Pith
  Annual rings
  Bark
  Cambium: has two parts—phloem and xylem

## Slide 6: Hardwoods and Softwoods (continued)
Parts of a tree (continued)
  Sapwood
  Heartwood
  Medullary rays

## Slide 7
Figure 9-3 Both walnut (top) and cherry (bottom) exhibit a striking difference in color between their heartwood and sapwood.
sapwood
sapwood
heartwood
heartwood

## Slide 8: Hardwoods and Softwoods (continued)
Foresters and loggers select trees to be cut for lumber
Trees are cut down and their limbs are removed
Trunks are bundled together and transported to a sawmill for processing
At the mill, logs are sorted by species

## Slide 9: Hardwoods and Softwoods (continued)
Best logs are set aside to be processed into cabinet-grade veneer
Bark is stripped off by a debarking machine
Logs go through metal detector to sort out logs containing metal
Majority of logs that are processed into lumber are squared up
  Squared-up log is called cant

## Slide 10: Hardwoods and Softwoods (continued)
Cants are sawn into boards
Edges of boards are trimmed to achieve uniform width; boards are cut to length
Boards go to the grader to be sorted
After grading, boards are packaged for drying

## Slide 11
Figure 9-11 Plainsawn and quartersawn lumber have a very different appearance.

## Slide 12: Hardwoods and Softwoods (continued)
After drying, we have roughsawn lumber
Depending on the tools a shop has, it may purchase roughsawn lumber
Lumber not sold as roughsawn is surfaced
Most of the lumber purchased by cabinetmakers is surfaced two sides (S2S)

## Slide 13: Moldings
Wood pieces with shaped edges
  Used cover transitions between surfaces
  Act as decorative elements
Moldings are used in home construction
  Decorate the edges of doors and windows
  Floor/wall and wall/ceiling intersections
Purchased by the type, size, grade, and length

## Slide 14: Lumber Defects
Common natural defects
  Knot
  Blue stain
  Pitch pocket
  Bark pocket

## Slide 15: Lumber Defects (continued)
Defects that occur in milling and drying
  Warp
  Bow
  Crook
  Cup
  Twist
  Kink
  Wane

## Slide 16: Lumber Defects (continued)
Defects that occur in milling and drying (continued)
  Split
  Check
  Shake
  Case hardening
  Honeycombing

## Slide 17: Lumber Grades
Softwood grades
  Standards set by associations of lumber producers
  Must conform to U.S. Department of Commerce American Lumber Standards
    American Softwood Lumber Standard PS 20-70
  Based on structural integrity of a board
  Two broad categories
    Construction
    Remanufacture

## Slide 18: Lumber Grades (continued)
Hardwood grades
  Standards established by National Hardwood Lumber Association (NHLA)
  Based on the amount of clear wood that can be cut from each board
  Standard grades form the framework by which all American hardwoods are traded
  Both sides of the board must meet the minimum requirements

## Slide 19: Lumber Grades (continued)
Softwood lumber
  Sold in standard thicknesses, widths, and lengths
  Ordered by its nominal size
  Sold by the individual piece

## Slide 20: Lumber Grades (continued)
Hardwood lumber
  Estimated and sold by the board foot, rather than by the piece
  Widths and lengths are not standardized
  Thickness of the piece is indicated by the quarter of an inch, and not in whole inches

## Slide 21: Lumber Grades (continued)
Strength of any wooden component is determined by its grain and how that grain is oriented on the furniture component
Also affects stability of the material, gluing properties, and finishing
Types of grain
  End grain, longitudinal grain, edge grain, face grain, radial grain, and tangential grain

## Slide 22
Figure 9-27 A board exhibiting radial grain on its face was cut along a radius running from the center of the tree outward.

## Slide 23
Figure 9-29 A board showing tangential grain on its face was cut tangent to the growth rings of the tree.

## Slide 24: Lumber Grades (continued)
Wood movement
  Wood is not a static material
    Expands and contracts in response to changes in relative humidity
  As we build furniture, we have to allow for this movement
  The way wood moves is directly related to its grain
    Greatest amount of movement takes place tangent to the grain

## Slide 25: Lumber Grades (continued)
Home centers
Retail lumber stores
Hardwood mills
Can have trees of your own cut and milled by a portable band saw mill

## Slide 26: Lumber Grades (continued)
Structures slated for demolition
Local road crews
Power companies
Mail order and online

## Slide 27: Summary
Wood is a beautiful yet complex material
Understanding how wood grew and was milled and seasoned gives us vital tools for working with it successfully
Appearance of wood and its behavior relative to the surrounding environment are largely determined by the roles the wood played in the original tree